## Slide 1: Advanced New Hardware Optimized for Policy Enforcement Arun Thomas arun@draper.com Chris Casinghino ccasinghino@draper.com Arch Owen aowen@draper.com Jeff Opper jopper@draper.com

## Slide 2: HOPE Innovations
A single, unified hardware-software security architecture can cover all 7 SSITH CWE vulnerability classes
  Every word has metadata. Every instruction is checked.
Supports flexible security micropolicies
  Policies are defined in software, not baked into hardware
Formal specification and verification gives precise guarantees of security and high assurance of correctness
PPASS Workbench aids designer in customizing security architectures/policies for PPASS requirements

## Slide 3: Draper HOPE
Programmable Metadata Tags
  Each data word has a programmable tag.
  Cannot be modified by user application.
Micropolicies
  Define security, safety, or correctness requirements.
Processor Interlocks for Policy Enforcement (PIPE)
  Unassailable hardware interlock enforces policies.
  Runs parallel to application processor.
HOPE adds 3 elements to an existing architecture to create defensible hardware
HOPE
Hardware
HOPE
Embedded
Software
HOPE element

## Slide 4: PIPE Diagram
PIPE: Processor Interlocks for Policy Enforcement

## Slide 5: Metadata Tags
Each memory word and register has a programmable metadata tag.
At every instruction, tags for the relevant memory and registers are passed to the PIPE.
Application cannot directly create or modify tags.
Tags can be pointers to arbitrary data structure, enabling complex policies.
metadata tag | data payload
Example metadata:
Provenance
Access rights
Object type
Executable?
Legal branch target?
Buffer bounds
Instruction, user data, etc.

## Slide 6: Micropolicies
Policies define what instructions are allowed and how metadata is updated.
Policies are written in a domain-specific rule language.
PIPE sends metadata tags to policies running on the policy execution core.
Policies check metadata against installed rules and reject bad behavior.
Example Policies
Heap Safety
Stack Safety
Control-flow Integrity
Compartmentalization
Information Flow Control
Domain-specific policies